## Slide 1: CubeSat
Design space exploration and optimization David Malawey Hung Nguyen
For Course Final Presentation
► Texas A&M Engineering – ME689
► Multidisciplinary Systems Design and Optimization
► Professor: Dr. Douglas Allaire
► Semester: Spring 2015, College Station Campus
(team project for preliminary work, with DM & HN followed by individual work DM for utilization in masters thesis)

## Slide 2: Contents:
Problem Formulation
  Motivation and Challenges
  Objectives and Constraints
Model and Simulation
  Model Overview and Description
  Benchmarking and Validation
Optimization
  Algorithms and tuning
  Post Optimality Analysis
  Multi-Objective and Tradeoff Analysis
Conclusions and Recommendations

## Slide 3: Problem Formulation
Motivation
  Over 200 cubesats flown, industry growing.
  Typical Missions:
    measure radiation
    take photos of earth
    microgravity experiments
    Test a small scale system before implementing a multi-million $ satellite
  Design a framework that can be reoptimized for different missions
  Determine the best configuration as the actual project moves forward
    Capstone team is developing a “motherboard.”
    Estimates will be converted to hard parameters over time and testing.
    Take advantage of heuristic data from previous designs
Challenges
  Lack of heuristic data (for example, velocity vector disturbance)
  Lack of expertise in each module (ie thruster design)
  Budgeting the physical volume
Background Photo: Planet labs Doves aim to create a constellation that images earth every 24 hours.

## Slide 4: Problem Formulation
Design Vector |  |  |  |  | 
X(1) | X(2) | X(3) | X(4) | X(5) | X(6)
Propellant | Thruster type | Structure material | Solar Panels | Batteries | Structure rail width
Hydrogen Helium Neon Nitrogen Argon Krypton Xenon Freon 14 Methane Ammonia | Moog Marotta Lee LHDB | 6061 T6 Aluminum Titanium A36 Steel | Integers 0~4 | Integers 1~unlimited | 3mm~inf
Marotta micro thruster
Objectives | Parameters | Constraints
Min Mass | Mission duration | (1) Power required
Min Cost | Solar Panel Power | (2) Structure bending stiffness
 | Battery Capacity | (built in) propellant sufficient
 | Flight Disturbance | 
 | Volume of a propellant tank | 
Notes: David

## Slide 5: Model and Simulation
Model Overview
  Each module outputs a matrix of all variables
Design vector
Structure
Propulsion
Battery/Power
Cost
Mass
Notes: David

## Slide 6: Model and Simulation
Benchmarking
  Structures, materials, rigidity, manufacturability
CubeSatKit.com GomSpace.com Brown University
  Cost and Mass can be benchmarked by component.
  Cost
    Cubesatkit.com $7500 (frame and microcontroller board)
  Mass
    Cubesatkit.com 300g (frame and microcontroller board)
  Parameters such as solar panel wattage taken directly from suppliers.
Notes: David

## Slide 7: Model and Simulation
Validation
  Design vector:
    Xenon: used by NASA miniAERcam system
    The Lee Co thruster used by Micro Aerospace Solutions, Inc.
    6061 Aluminum used by most designs
    Solar panels: usually maximized. (folding panels also implemented)
  Breakdown variables:
NASA MiniAERcam
Micro Aerospace Solutions Thruster Module
Notes: David

## Slide 8: Design Space Exploration
We have 6 factors and 3 levels, doing a full factorial design would take experiments.
orthogonal array instead of full factorial
We evaluated the main effect each factor level on cost and mass separately and then find the level with best effect on both cost and mass.
Factor | Level 1 | Level 2 | Level 3
Propellant | Hydrogen (1) | Nitrogen (4) | Xenon (7)
Thruster type | moog | marotta | lee LHDB0542115H
Structure material | Al 6061 T6 | Titanium | A36 steel
#panels | 0 | 1 | 4
#batteries | 1 | 2 | 3
Structure rail width (m) | 0.003 | 0.006 | 0.008
Notes: Hung

## Slide 9: DOE Results
Variable (Factor) | Level | Cost ($E3) | ME Cost | Mass (kg) | Me Mass
Propellant | Hydrogen | $8.633 | -$0.070 | 3.586 | $1.512
 | Nitrogen | $8.654 | -$0.049 | 1.301 | -$0.773
 | Xenon | $8.822 | $0.119 | 1.335 | -$0.739
Thruster Type | moog | $8.322 | -$0.381 | 1.853 | -$0.221
 | marotta | $8.690 | -$0.013 | 2.428 | $0.355
 | lee LHDB0542115H | $9.096 | $0.393 | 1.940 | -$0.134
Structure Material | Al 6061 T6 | $8.633 | -$0.069 | 1.928 | -$0.145
 | Titanium | $8.822 | $0.119 | 1.873 | -$0.201
 | A36 steel | $8.653 | -$0.050 | 2.420 | $0.346
Number of Panel | 0 | $8.139 | -$0.564 | 1.373 | -$0.701
 | 1 | $8.723 | $0.020 | 1.811 | -$0.263
 | 4 | $9.089 | $0.386 | 2.800 | $0.726
Number of Battery | 1 | $5.888 | -$2.815 | 1.685 | -$0.388
 | 2 | $8.724 | $0.021 | 1.998 | -$0.076
 | 3 | $11.496 | $2.793 | 2.538 | $0.464
Structure Width (m) | 0.003 | $8.710 | $0.007 | 1.462 | -$0.612
 | 0.006 | $8.639 | -$0.064 | 1.879 | -$0.195
 | 0.008 | $8.784 | $0.081 | 3.081 | $1.007
Notes: Hung

## Slide 10: Single-objective Optimization
Heuristic GA
  finds global area of interest
  Propellant, Thruster, Material
SQP
  Local analysis
  Solar Panels, Batteries, Structure width
Coupled analysis
  X(1~3) passed from GA to SQP
GA939g
SQP921g

## Slide 11: Multiple-objective Optimization
AWS Pareto Front
 | Prop | Thruster | Material | S.Panel | Battery | Rail (mm) | Cost | Mass (g)
A | Freon | Lee | Titanium | 0.690 | 1 | 3.04 | $6,333 | 802
B | Xenon | Lee | Aluminum | 0.690 | 1 | 6.354 | $6,312 | 921
C | Methane | Marotta | Steel | 0.760 | 1 | 3.00 | $5,798 | 1,293
C
B
A
NBI Toolbox Pareto Front

## Slide 12: Post Optimality Analysis
Sensitivity Analysis
J
The normalized gradient vector is
Chart: Sensitivity of non-discrete variables
| Cost | Mass
# S. Panel | 0.99347 | 0.99966
# Battery | 0.98903 | 0.9995
Structure width | 0.99342 | 0.99581
Notes: Hn

## Slide 13: Conclusion and Recommendation
Conclusion about our methodology:
DOE is inexpensive and works great for finding initial starting point
Heuristic methods is expensive and subjective to tuning
SQP works great for local optimization but doesn’t handle discrete variables well
Recommendation:
Increase fidelity of model for future development by making better assumption
  Example: thruster nozzle.
Hybrid solution: DOE -> Heuristic -> SQP
Questions…
Notes: HN

## Slide 14: Sources:
http://aercam.jsc.nasa.gov
www.cubesatkit.com
A Propulsion System Taylored to Cubesat Applications, Donald Platt, Micro Aerospace Solutions, inc.
www.planet.com